## Slide 1: SOFT354: Parallel Computation and distributed systems
Week 5
Dr Robert Merrison-Hort

## Slide 2: This week’s lecture
Compute to global memory access (CGMA) ratio for simple and shared memory matrix multiplication.
Quickly look at a couple of common workshop issues.
Convolution:
  What is it
  Simple 1D convolution kernel
  Shared memory 1D convolution kernel
  Performance comparison

## Slide 3: reminder
Practice test next week: Thursday 3th November.
In the usual lecture slot / room.
Doesn’t count towards your mark (but take it seriously!)
Short sentence / single word / number answers only.
Bring a calculator (though there shouldn’t be anything you can’t work out in your head / on paper).

## Slide 4: CGMA for matrix multiplication
Compute to global memory access ratio:
Last week’s homework: what’s the CGMA of the simple and shared memory matrix multiplication kernels?

## Slide 5: CGMA for matrix multiplication
How many floating point operations will a block do?
Each thread does a dot product of one column (from A) with one row (from B).
In an nxn matrix, this will involve multiplying together n pairs of values (n FLOP) and adding them up (n-1 FLOP).
A block has mxm threads, so it will do:
Floating point operations.
? | ?
? | ?
1 | 2
3 | 4
5 | 6
7 | 8
A
B

## Slide 6: CGMA for matrix multiplication
This gives us the ‘C’ part of the ratio:
The global memory access part is different for the simple and shared memory algorithms.

## Slide 7: CGMA for matrix multiplication
Simple algorithm:
  Each thread accesses all the elements of one row and one column  2n accesses.
  It also writes its result back to global memory (+1 access).
  A block contains mxm threads, so will read/write:
  Floats to/from global memory.
Rubbish!
Notes: When n is relatively large the -1 and +1 have basically no effect so we can ignore them. For example, if n=100, (2n-1)/(2n+1)=0.99

## Slide 8: CGMA for matrix multiplication
Shared memory algorithm:
  The threads in a block co-operate to load the elements of the matrix, such that each element is only fetched from global memory once  2mn global memory reads.
  Each thread also has to write its result, so mxm writes.
  So in total a block will do accesses.
Notes: When n is relatively large the -1 and +1 have basically no effect so we can ignore them. For example, if n=100, (2n-1)/(2n+1)=0.99

## Slide 9: CGMA for matrix multiplication
For n=1000:
More on CGMA later in the lecture…
Chart: Block Dimension (m)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200
Simple Algorithm | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999 | 0.999
Shared Memory Algorithm | 9.9453 | 19.7921 | 29.5419 | 39.1961 | 48.7561 | 58.2233 | 67.599 | 76.8846 | 86.0813 | 95.1905 | 104.2133 | 113.1509 | 122.0047 | 130.7757 | 139.4651 | 148.0741 | 156.6037 | 165.055 | 173.4292 | 181.7273

## Slide 10: Some common workshop problems
The expression sizeof(someVar) is replaced with the size (in bytes) of someVar at compile time.
So if you have a statically allocated array:
float h_array[128];
__device__ float d_array[128];
You can get its size with sizeof:
sizeof(h_array) == sizeof(d_array) == 128*sizeof(float) == 512

## Slide 11: Some common workshop problems
But if you have a dynamically allocated array:
float* h_array = (float*)malloc(128*sizeof(float));
float* d_array = NULL;
cudaMalloc(&d_array, 128*sizeof(float));
The size isn’t known at compile time. Instead, sizeof will give you the size of a pointer:
sizeof(h_array) == sizeof(d_array) == sizeof(inData) == 4
Or an array argument to a function / kernel:
void myFunction(float* inData) {
You need to keep track of how big your dynamically allocated arrays are!
Notes: On a 32-bit system. In 64-bit, a pointer is 8 bytes.

## Slide 12: Some common workshop problems
If you have statically allocated device variables:
__device__ float d_array[128];
__constant__ float d_const[16];
Copy to/from them using cudaMemcpy*Symbol:
cudaMemcpyToSymbol(d_const, h_const, sizeof(h_const));
cudaMemcpyFromSymbol(h_array, d_array, sizeof(d_array));
Note: don’t specify a direction – it will interpret this as an offset and probably give an error!

## Slide 13: Some common workshop problems
If you have dynamically allocated device variables:
float* d_array;
cudaMalloc(&d_array, 128*sizeof(float));
Copy to/from them using cudaMemcpy:
float h_array[128];
cudaMemcpy(d_array, h_array, sizeof(h_array),
cudaMemcpyHostToDevice);
cudaMemcpy(h_array, d_array, sizeof(h_array),
cudaMemcpyDeviceToHost);

## Slide 14: convolution
Hopefully you’ve already seen convolution if you’ve done this week’s workshop.
Mathematical operator – technically we’re looking at discrete convolution.
Usually used in one or two dimensions.

## Slide 15: 1d Convolution applications
Acoustic modelling: simulate different environments by convolving audio signal with a recording of an “impulse” made in the environment.
Signal processing: e.g. high/low pass filters.
Statistics: e.g. moving average of some data is a 1D convolution.

## Slide 16: 2D+ Convolution applications
Image processing: e.g. blurring, sharpening, edge detection.
Computational fluid dynamics.
Convolutional neural networks.
Radiotherapy planning systems.

## Slide 17: 1d convolution example
Simple moving average.
Can use to smooth out noise from signals:
Raw neuron recording
5-point smoothed (twice)
Notes: Recording of a tadpole neuron by Stella Koutsikou at Bristol University.

## Slide 18: Simple moving average
1D array of input data:
0.1
0.2
0.3
0.4
0.3
0.2
0.1
0.2
0.3
0.4
0.3
Replace each element with the average of itself and its two neighbours on each side (5-point average).
1D array of output data:

## Slide 19: Simple moving average
1D array of input data:
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
Replace each element with the average of itself and its two neighbours on each side (5-point average).
1D array of output data:
0.2
0.2

## Slide 20: Simple moving average
1D array of input data:
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
Replace each element with the average of itself and its two neighbours on each side (5-point average).
Need to do this for each element.
1D array of output data:
0.2
0.2
0.24

## Slide 21: Simple moving average
1D array of input data:
0.1
0.2
0.3
0.4
0.3
0.4
0.3
Replace each element with the average of itself and its two neighbours on each side (5-point average).
Need to do this for each element.
1D array of output data:
0.2
0.2
0.24
0.3
0.1
0.22

## Slide 22: Simple moving average
This is equivalent to convolving the data with the following mask*:
0.2
0.2
0.2
0.2
0.2
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.08
0.06
0.04
0.02
0.04
0.24
0.24
* More commonly called a kernel, but we’ll use “mask” to avoid confusion with CUDA kernels.

## Slide 23: Simple moving average
This is equivalent to convolving the data with the following mask:
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.06
0.04
0.02
0.04
0.06
0.22
0.24
0.1
0.2
0.3
0.4
0.3
0.4
0.3
0.2
0.2
0.3
0.1
0.22

## Slide 24: Boundary conditions
?
?
How do we calculate the values at the edges?
0.1
0.2
0.3
0.4
0.3
0.4
0.3
0.2
0.2
0.3
0.1
0.2
0.2
0.2
0.2
0.2
Various options…
  Extend the first / last elements:
0.2
0.2
0.2
0.2
0.2
0.3
0.3
0.1
0.2
0.3
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.1
0.1

## Slide 25: Boundary conditions
?
?
How do we calculate the values at the edges?
0.1
0.2
0.3
0.4
0.3
0.4
0.3
0.2
0.2
0.3
0.1
0.2
0.2
0.2
0.2
0.2
Various options…
  Wrap around to the start:
0.3
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.2
0.2
0.2
0.2
0.2
0.1
0.2
0.3

## Slide 26: Boundary conditions
?
?
How do we calculate the values at the edges?
0.1
0.2
0.3
0.4
0.3
0.4
0.3
0.2
0.2
0.3
0.1
0.2
0.2
0.2
0.2
0.2
Various options…
  Skip the end elements:
0.3
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.1
0.2
0.3
Don’t convolve these
Don’t convolve these

## Slide 27: Boundary conditions
?
?
How do we calculate the values at the edges?
0.1
0.2
0.3
0.4
0.3
0.4
0.3
0.2
0.2
0.3
0.1
0.2
0.2
0.2
0.2
0.2
Various options…
  Skip the end elements:
0.3
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.1
0.2
0.3
Don’t convolve these
Don’t convolve these
Output is smaller than input.

## Slide 28: Other moving average masks
7 point simple moving average:
Weighted 5 point moving average:
0.1
0.2
0.4
0.2
0.1
3 point trailing average:
0
0
Note: masks are normalised – all elements add up to 1.
Any 1D discrete convolution (e.g. for audio processing) is defined by its mask, which is just an array of values.

## Slide 29: Quick exercise
Convolve this data:
1
2
2
3
22
20
21
21
With this mask:
-1
2
-1
(Extend the boundary elements)
What is this mask doing?
Notes: The result should be [-1, 1, -1, -18, 21, -3, 1, 0]. The convolution is doing one dimensional edge detection (it’s similar to the 2D mask you used in the workshop) – it outputs a high value where the input data abruptly changes by a large amount.

## Slide 30: Parallelising 1D convolution
Strategy: each thread calculates one output value.
0.2
0.4
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.3
0.1
0.1
0.2
0.2
0.2
0.2
0.2
0.3
0.3
0.2
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.3
0.1
0.1
0.2
0.2
0.2
0.2
0.2
0.3
0.1
Thread 0
0.3
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.3
0.1
0.1
0.2
0.2
0.2
0.2
0.2
0.1
0.4
0.2
Thread 1
Thread 2
Etc…
0.1

## Slide 31: Code!
// Input and output arrays (N = problem size)
const int N = 1000;
__device__ float d_input[N];
__device__ float d_output[N];
// Convolution mask.
const int M = 5;
__constant__ float d_mask[M] = { 0.2f, 0.2f, 0.2f, 0.2f, 0.2f};
// Adjust an index so that elements on the ends of
// the input repeat infinitely.
__device__ __host__ int getIndexRepeatBounds(int index)
{
if (index < 0) return 0;
if (index >= N) return N - 1;
return index;
}

## Slide 32: Code!
// Input and output arrays (N = problem size)
const int N = 1000;
__device__ float d_input[N];
__device__ float d_output[N];
// Convolution mask.
const int M = 5;
__constant__ float d_mask[M] = { 0.2f, 0.2f, 0.2f, 0.2f, 0.2f};
// Adjust an index so that elements on the ends of
// the input repeat infinitely.
__device__ __host__ int getIndexRepeatBounds(int index)
{
if (index < 0) return 0;
if (index >= N) return N - 1;
return index;
}

## Slide 33: Code!
// Input and output arrays (N = problem size)
const int N = 1000;
__device__ float d_input[N];
__device__ float d_output[N];
// Convolution mask.
const int M = 5;
__constant__ float d_mask[M] = { 0.2f, 0.2f, 0.2f, 0.2f, 0.2f};
// Adjust an index so that elements on the ends of
// the input repeat infinitely.
__device__ __host__ int getIndexRepeatBounds(int index)
{
if (index < 0) return 0;
if (index >= N) return N - 1;
return index;
}

## Slide 34: Code!
// Simple 1D convolution kernel.
__global__ void convolveKernel()
{
int globalId = blockIdx.x*blockDim.x + threadIdx.x;
if (globalId < N) {
float conv = 0.0f;
for (int i = 0; i < M; i++) {
int inputIndex = globalId - M / 2 + i;
conv += d_input[getIndexRepeatBounds(inputIndex)]
* d_mask[i];
}
d_output[globalId] = conv;
}
}

## Slide 35: Code!
// Simple 1D convolution kernel.
__global__ void convolveKernel()
{
int globalId = blockIdx.x*blockDim.x + threadIdx.x;
if (globalId < N) {
float conv = 0.0f;
for (int i = 0; i < M; i++) {
int inputIndex = globalId - M / 2 + i;
conv += d_input[getIndexRepeatBounds(inputIndex)]
* d_mask[i];
}
d_output[globalId] = conv;
}
}

## Slide 36: Code!
// Simple 1D convolution kernel.
__global__ void convolveKernel()
{
int globalId = blockIdx.x*blockDim.x + threadIdx.x;
if (globalId < N) {
float conv = 0.0f;
for (int i = 0; i < M; i++) {
int inputIndex = globalId - M / 2 + i;
conv += d_input[getIndexRepeatBounds(inputIndex)]
* d_mask[i];
}
d_output[globalId] = conv;
}
}

## Slide 37: Code!
// Simple 1D convolution kernel.
__global__ void convolveKernel()
{
int globalId = blockIdx.x*blockDim.x + threadIdx.x;
if (globalId < N) {
float conv = 0.0f;
for (int i = 0; i < M; i++) {
int inputIndex = globalId - M / 2 + i;
conv += d_input[getIndexRepeatBounds(inputIndex)]
* d_mask[i];
}
d_output[globalId] = conv;
}
}

## Slide 38: using shared memory
Assume the threads are organised into blocks of four.
0.2
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.1
Block 0 convolves these elements.
Block 1 convolves these elements.
Block 2 convolves these elements.
How many times is each element in global memory accessed by the threads in block 1?
  Mask size (M) = 5
0.2
0.4
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.1
0.3
|
|
|
|
|

## Slide 39: using shared memory
Assume the threads are organised into blocks of four.
0.2
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.1
Block 0 convolves these elements.
Block 1 convolves these elements.
Block 2 convolves these elements.
How many times is each element in global memory accessed by the threads in block 1?
  Mask size (M) = 5
0.2
0.4
0.4
0.2
0.3
0.1
0.3
0.3
0.1
|
||
||
||
||
0.3
0.2
|

## Slide 40: using shared memory
Assume the threads are organised into blocks of four.
0.2
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.1
Block 0 convolves these elements.
Block 1 convolves these elements.
Block 2 convolves these elements.
How many times is each element in global memory accessed by the threads in block 1?
  Mask size (M) = 5
0.2
0.4
0.4
0.2
0.3
0.3
0.3
0.1
|
||
|||
|||
|||
0.3
||
0.2
0.1
|

## Slide 41: using shared memory
Assume the threads are organised into blocks of four.
0.2
0.4
0.3
0.4
0.2
0.2
0.3
0.1
0.3
0.3
0.1
Block 0 convolves these elements.
Block 1 convolves these elements.
Block 2 convolves these elements.
How many times is each element in global memory accessed by the threads in block 1?
  Mask size (M) = 5
0.2
0.4
0.4
0.3
0.3
0.3
0.1
|
||
|||
||||
||||
0.3
|||
0.2
||
0.1
0.2
|

## Slide 42: using shared memory
20 global memory accesses across the block…
… but to only 8 different memory addresses.
If we just load each element that the block needs into shared memory once, would only need 8 global memory accesses  reduction of 60%.
(Caching will help somewhat anyway, but should still get an improvement using shared memory)
0.2
0.4
0.4
0.3
0.3
0.3
0.1
|
||
|||
||||
||||
0.3
|||
0.2
||
0.1
0.2
|

## Slide 43: Using shared memory
What is the improvement in general?
In the simple algorithm, how many global memory accesses does each block do?
Every thread needs to access one element for each value in the mask, so M accesses per thread.
If there are DB threads in a block, then total global memory accesses per block is M*DB.

## Slide 44: Using shared memory
How many global memory accesses do we need if we use shared memory (assume it’s big enough)?
Need the value at to each thread’s position:
The neighbour values are called halo / apron elements.
So total number of accesses is DB+M-1
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
(DB of these)
And also some neighbouring values:
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
(M-1 of these)

## Slide 45: Using shared memory
So for the simple case we have M*DB global memory accesses.
And in the shared memory case we have DB+M-1 global memory accesses.
Assume 32 threads per block (DB=32). If we increase the mask size (M) by 2, how many more global memory accesses for each method?
  Simple method: 2*32 = 64
  Shared memory method: 2
Improvement:

## Slide 46: implementation
Need to load DB+M-1 values from global memory…
… but only DB threads in the block.
So some threads will have to load multiple values.
Divide loading into phases.
Ceiling function (round up)

## Slide 47: implementation
The first element to be convolved by block i is i*DB.
  E.g. for block 1 (2nd block), DB=4:
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
Element 1*4
The first element to be loaded by block i is i*DB-M/2.
  E.g. for block 1, DB=4, M=5:
Integer division, so if M=5, M/2=2
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
Element 1*4-5/2

## Slide 48: implementation
Divide loading into phases.
So if DB=4, M=5: phases.
Shared memory for block 1
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
Phase 0
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 49: implementation
Divide loading into phases.
So if DB=4, M=5: phases.
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
0.4
0.3
0.3
0.2
Shared memory for block 1
Phase 0
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 50: implementation
Divide loading into phases.
So if DB=4, M=5: phases.
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
0.4
0.3
0.3
0.2
Shared memory for block 1
Phase 1
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 51: implementation
Divide loading into phases.
So if DB=4, M=5: phases.
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
0.4
0.3
0.3
0.3
0.2
0.1
0.2
Shared memory for block 1
0.4
Phase 1
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 52: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];

## Slide 53: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
Load one element for each thread in the block, plus M-1 halo elements at each end.
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
Db
sharedBufSize

## Slide 54: Code!
__global__ void convolveKernelShared()
{
// Load elements into shared memory (in phases)
int numPhases = (sharedBufSize) / Db;
if (((sharedBufSize) % Db) != 0) numPhases++;
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
Round up the number of phases.
Kernel Code

## Slide 55: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
int firstHaloIdx = blockIdx.x * Db - M / 2;
for (int p = 0; p < numPhases; p++) {
int offset = p*Db + threadIdx.x;
if (offset < sharedBufSize) {
d_shared[offset] =
d_input[getIndexRepeatBounds(firstHaloIdx + offset)];
}
}
__syncthreads();

## Slide 56: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
int firstHaloIdx = blockIdx.x * Db - M / 2;
for (int p = 0; p < numPhases; p++) {
int offset = p*Db + threadIdx.x;
if (offset < sharedBufSize) {
d_shared[offset] =
d_input[getIndexRepeatBounds(firstHaloIdx + offset)];
}
}
__syncthreads();
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2

## Slide 57: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
int firstHaloIdx = blockIdx.x * Db - M / 2;
for (int p = 0; p < numPhases; p++) {
int offset = p*Db + threadIdx.x;
if (offset < sharedBufSize) {
d_shared[offset] =
d_input[getIndexRepeatBounds(firstHaloIdx + offset)];
}
}
__syncthreads();
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2
E.g. offset for second thread (index 1) in phase 0

## Slide 58: Code!
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];
int firstHaloIdx = blockIdx.x * Db - M / 2;
for (int p = 0; p < numPhases; p++) {
int offset = p*Db + threadIdx.x;
if (offset < sharedBufSize) {
d_shared[offset] =
d_input[getIndexRepeatBounds(firstHaloIdx + offset)];
}
}
__syncthreads();
E.g. offset for second thread (index 1) in phase 1
0.2
0.4
0.4
0.3
0.3
0.3
0.1
0.3
0.2
0.1
0.2

## Slide 59: Code!
int globalId = blockIdx.x*blockDim.x + threadIdx.x;
if (globalId < N) {
float conv = 0.0f;
for (int i = 0; i < M; i++) {
conv += d_shared[threadIdx.x + i] * d_mask[i];
}
d_output[globalId] = conv;
}
}
// Number of threads per block.
const int Db = 4;
// Total number of elements to load into shared memory.
const int sharedBufSize = Db + M - 1;
// Shared memory.
__shared__ float d_shared[sharedBufSize];

## Slide 60: Results
N=10,000; vary mask size (M)
Apply convolution 1,000 times (to get bigger numbers).
Chart: Mask Size (M)
| 5 | 11 | 15 | 21 | 35 | 51
Simple Kernel | 97 | 134 | 203 | 245 | 287 | 365
Shared Memory Kernel | 133 | 177 | 152 | 182 | 223 | 258
For small mask sizes the simple kernel is faster!
More complicated shared memory kernel has some extra overheads, which outweigh the benefits with small M.

## Slide 61: Results
N=10,000; vary mask size (M)
Apply convolution 1,000 times (to get bigger numbers).
Chart: Mask Size (M)
| 5 | 11 | 15 | 21 | 35 | 51
Simple Kernel | 97 | 134 | 203 | 245 | 287 | 365
Shared Memory Kernel | 133 | 177 | 152 | 182 | 223 | 258
For larger masks, shared memory version is much faster.
E.g. M=51, 365ms vs 258ms (30% faster)

## Slide 62: CGMa ratio
How many computations does each block do?
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.08
0.06
0.04
0.02
0.04
0.24
Notes: Note that we’re only actually interested in how many useful computations the kernel does – i.e. ones that are directly part of the convolution. We’re ignoring the other operations (e.g. calculating indexes and offsets).

## Slide 63: CGMa ratio
How many computations does each block do?
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.08
0.06
0.04
0.02
0.04
0.24
Each thread does M multiplications…

## Slide 64: CGMa ratio
How many computations does each block do?
0.1
0.2
0.3
0.4
0.3
0.1
0.3
0.4
0.3
0.2
0.2
0.2
0.2
0.2
0.2
0.2
0.08
0.06
0.04
0.02
0.04
0.24
Each thread does M multiplications…
… and (M-1) additions.
And there are DB threads in a block.
So a block does DB * (M + (M-1)) computations.
= DB * (2M – 1)

## Slide 65: CGMA ratio
How many floating point values does each block have to read/write to/from global memory?
  (assume no caching…)
Simple kernel:
  Each thread loads M elements.
  Also has to store 1 element (its result).
  There are DB threads in a block.
  So each block reads/writes DB*(M+1) values.
  CGMA =
Rubbish!
Notes: For larger values of M the -1 and +1 don’t really have much effect, so we can ignore them. This leaves 2M/M, which is 2.

## Slide 66: CGMA ratio
How many floating point values does each block have to read/write to/from global memory?
  (assume no caching…)
Shared memory kernel:
  Each block as a whole loads DB+M-1 values.
  Also has to store DB elements (its results).
  So each block reads/writes 2DB+M-1 values.
  CGMA =
Notes: For larger values of M the -1 and +1 don’t really have much effect, so we can ignore them.

## Slide 67: CGMA ratio
As the mask size increases, CGMA reaches its theoretical limit of 2*DB=54 for the shared memory kernel.
Whereas in the simple kernel its limit is 2.
Chart: Mask Size (M)
Threads per block (DB)=27

## Slide 68: CGMA ratio
With modern GPUs aim for CGMA > 30.
On GTX480 memory bandwidth is 177GB/s = 44k floats / s.
CGMA=2  max. utilized processing power is 44*2=88 GFLOPS
Card capacity is 1,345 GFLOPS  memory limits us!
Chart: Mask Size (M)
Threads per block (DB)=27

## Slide 69: CGMA ratio
If CGMA is 54, max. utilized processing power is 44*54=2,376 GFLOPS
Card capacity is 1,345 GFLOPS  memory isn’t the limitation.
Chart: Mask Size (M)
Threads per block (DB)=27

## Slide 70: occupancy
Recall that occupancy is how many threads can be resident in one streaming multiprocessor at once.
Want to maximize this!
The available shared memory can be a limiting factor.

## Slide 71: occupancy
In CC 3.0, there can be up to 16 blocks per multiprocessor, but they share 48KB of shared memory.
This means to use the full 16 blocks, each block is limited to 48/16 = 3KB of shared memory.
In the shared memory kernel, each block loads DB+M-1 values into shared memory  (DB+M-1)*4 bytes.

## Slide 72: occupancy
To avoid shared memory limiting occupancy, we need
If we take DB = the maximum block size (2048 max. threads / 16 max. blocks = 128 threads):
So masks bigger than 641 elements will reduce occupancy.
Notes: 3072 = 3*1024 = 3KB

## Slide 73: occupancy
Is this true in practice?
  Yes!
From my laptop (CC3.0):
M=640
M=641
M=642
M=641
Notes: The three lines in the upper-right diagram are for the different possible configurations of shared memory / L1 cache. You can choose 48K of shared memory and 16K of L1, or 48K of L1 and 16K of shared, or 32KB of each (“Equal”).

## Slide 74: Questions
You can configure CUDA so that each SM has 16KB of shared memory instead of 48KB. On a CC3.0 card, at what mask size would shared memory limit occupancy if there was only 16KB available?
On a CC2.x card, at what mask size would shared memory limit occupancy if there was 48KB available?
Each block loads DB+M-1 values into shared memory  (DB+M-1)*4 bytes.
Notes: In the configuration where there is only 16KB of shared memory, L1 cache is increased to 48KB.

## Slide 75: Questions
You can configure CUDA so that each SM has 16KB of shared memory instead of 48KB. On a CC3.0 card, at what mask size would shared memory limit occupancy if there was only 16KB available?
Each block loads DB+M-1 values into shared memory  (DB+M-1)*4 bytes.
Maximum block occupancy is 16  1KB of shared memory each.
Maximum thread occupancy is 2048  DB=128
Notes: In the configuration where there is only 16KB of shared memory, L1 cache is increased to 48KB.

## Slide 76: Questions
On a CC2.x card, at what mask size would shared memory limit occupancy if there was 48KB available?
Each block loads DB+M-1 values into shared memory  (DB+M-1)*4 bytes.
Maximum 1,536 threads per SM, 8 blocks
   set DB=1536/8=192
48KB shared memory, divided by 8 blocks = 6KB each.
CC2 has the same amount of shared memory but fewer maximum resident blocks  each block can use more shared memory.

## Slide 77: 2d Convolution
Basically the same, except now you have 2D data, a 2D mask, and a 2D grid of threads.
0.89 | 0.67 | 0.61 | 0.17
0.68 | 0.70 | 0.11 | 0.56
0.19 | 0.91 | 0.76 | 0.18
0.31 | 0.05 | 0.15 | 0.77
1 | 4 | 7
2 | 5 | 8
3 | 6 | 9
0.89*0 | 0.67*0 | 0.61*0 | 0.17*0
0.68*0 | 0.70*1 | 0.11*4 | 0.56*7
0.19*0 | 0.91*2 | 0.76*5 | 0.18*8
0.31*0 | 0.05*3 | 0.15*6 | 0.77*9
Data (convolve shaded element)
Kernel
Add coloured values together to get new value for the red element.

## Slide 78: 2d convolution
Can handle boundaries by repeating elements:
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.68 | 0.68 | 0.70 | 0.11 | 0.56 | 0.56
0.19 | 0.19 | 0.91 | 0.76 | 0.18 | 0.18
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
Or the other techniques (wrapping, skipping).

## Slide 79: Shared memory 2d convolution
Assume four DBxDB blocks:
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.68 | 0.68 | 0.70 | 0.11 | 0.56 | 0.56
0.19 | 0.19 | 0.91 | 0.76 | 0.18 | 0.18
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
DB=2
Each block has to load (DB+1)2 elements.

## Slide 80: Shared memory 2d convolution
Assume four DBxDB blocks:
DB=2
Each block has to load (DB+M-1)2 elements.
Divide loading into phases.
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.68 | 0.68 | 0.70 | 0.11 | 0.56 | 0.56
0.19 | 0.19 | 0.91 | 0.76 | 0.18 | 0.18
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77

## Slide 81: Shared memory 2d convolution
Assume four DBxDB blocks:
DB=2
Each block has to load (DB+M-1)2 elements.
Divide loading into phases.
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.89 | 0.89 | 0.67 | 0.61 | 0.17 | 0.17
0.68 | 0.68 | 0.70 | 0.11 | 0.56 | 0.56
0.19 | 0.19 | 0.91 | 0.76 | 0.18 | 0.18
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
0.31 | 0.31 | 0.05 | 0.15 | 0.77 | 0.77
Phase 0
Phase 1
Phase 2
Phase 3

## Slide 82: summary
Convolution is a very important mathematical operation with many applications.
On the GPU convolution can be sped up greatly (esp. when M is large) by using shared memory.
Seen a couple of examples of calculating compute to global memory access ratios: aim for > 30.
Beware: shared memory can limit occupancy.